SPECIAL DOORS			SECTION 08 38 00

PART 1 - GENERAL

1.1	RELATED DOCUMENTS

A.	Drawing and general provisions of the Contract, including General and

Supplementary Conditions and Division 1 Specification Sections, apply to this

Section.

1.2	SUMMARY

A.	This section includes traffic doors and frames

1.3	SUBMITTALS

A.	Product Data:  For each type of door and frame indicated.  Include construction

details relative to materials, individual components and profiles, finishes and fire

ratings (if required) for access doors and frames.

B.	Shop Drawings:  Show fabrication and installation details of traffic doors and

frames.  Include plans, elevations, sections, details and attachments to other

Work.

PART 2 - PRODUCTS

2.1	ACCEPTABLE MANUFACTURERS/PRODUCTS

A.	Traffic Door Manufacturer:  Subject to compliance with requirements, provide

products of the following:

www.restaurantdoors.com

2.2	TRAFFIC DOORS AND FRAMES

A.	 Lightweight Stainless Steel Service Doors

# 1.	Door shall be constructed of 16 gauge stainless steel with #4 brush 				finish.

2.	Panels shall be manufactured with a formed triangular leading edge and back edge spine.

08 38 00 – 1

3	Standard Hinge System:  Doors shall utilize stainless steel adjustable gravity close hardware system with panel mounted hinge body, and stainless steel jamb mounting bracket. Hinge shall utilize stainless steel covers.

4	Bottom hinge assembly shall be 5/8" diameter stainless steel pin

with panel mounted saddle bracket and shall include hardware for floor

and jamb mount installation.

5.	Window shall be 9" x 14" shatter resistant acrylic, set in black rubber

molding.  All windows shall be factory installed and sealed. Window shall

be centered 60" from the floor.

2.3	FABRICATION

A.	General:  Provide traffic door assemblies manufactured as integral units ready

for installation.

B.	Metal Surfaces:  For metal surfaces exposed to view in the completed Work,

provide materials with smooth, flat surfaces without blemishes.  Do not use

materials with exposed pitting, seam marks, roller marks, rolled trade names or

roughness.

# 2.4	WARRANTY

A.	365 days from the date of installation or 395 days from the date of

shipment, whichever comes first.

PART 3 - EXECUTION

A.	Install special doors complete with necessary hardware and accessories in

accordance with final shop drawings, manufacturer's instructions and as

specified herein.

B.	All assemblies must be installed plumb, level and properly aligned.

C.	Upon completion of installation, lubricate, test and adjust doors to operate

easily, free from warp, twist or distortion.

D.	Coordinate installation of bollards and/or wall stops with architectural drawings.

- END OF SECTION 08 38 00 -

08 38 00 -2