SPECIAL DOORS			SECTION 08 38 00

PART 1 - GENERAL

1.1	RELATED DOCUMENTS

A.	Drawing and general provisions of the Contract, including General and

Supplementary Conditions and Division 1 Specification Sections, apply to this

Section.

1.2	SUMMARY

- This section includes traffic doors

- Frame installers shall coordinate opening sizes with door manufacturer and specifications.

- Door frames not included in this section.

1.3	SUBMITTALS

A.	Product Data:  For each type of door.  Include construction details relative to materials, individual components and profiles, finishes and fire

ratings (if required) for access doors and frames.

B.	Shop Drawings:  Show fabrication and installation details of traffic doors and

frames.  Include plans, elevations, sections, details and attachments to other

Work.

PART 2 - PRODUCTS

2.1	ACCEPTABLE MANUFACTURERS/PRODUCTS

A.	Traffic Door Manufacturer:  Subject to compliance with requirements, provide

products of the following:

Restaurantdoors.com

2.2	TRAFFIC DOORS

A.	 Traditional Wood Core Doors

- Doors shall be constructed of 3/4" thick solid wood core with .032 high

pressure laminate on both sides.

- Door shall be manufactured with stainless steel  impact plates 48

high on both sides of panel.

3.	All edges shall be covered with stainless steel edge trim.

4.	Doors shall stainless steel adjustable gravity close hardware

system with panel mounted hinge body, and stainless steel jamb

mounting bracket.  Removable covers allow for hinge adjustment during

installation.

5.	Bottom hinge assembly shall be 1/2" diameter powder stainless steel pin

with panel mounted saddle bracket and shall include hardware for floor

and jamb mount installation.

6.	Window shall be 9" x 14" shatter resistant acrylic, set in black rubber

molding.  All windows shall be factory installed and sealed. Window shall

be centered 60" from the floor.

2.3	FABRICATION

A.	General:  Provide traffic door assemblies manufactured as integral units ready

for installation.

B.	Metal Surfaces:  For metal surfaces exposed to view in the completed Work,

provide materials with smooth, flat surfaces without blemishes.  Do not use

materials with exposed pitting, seam marks, roller marks, rolled trade names or

roughness.

# 2.4	WARRANTY

A.	365 days from the date of installation or 395 days from the date of

shipment, whichever comes first.

PART 3 - EXECUTION

A.	Install special doors complete with necessary hardware and accessories in

accordance with final shop drawings, manufacturer's instructions and as

specified herein.

B.	All assemblies must be installed plumb, level and properly aligned.

08 38 00 -2

C.	Upon completion of installation, lubricate, test and adjust doors to operate

easily, free from warp, twist or distortion.

D.	Coordinate installation of bollards and/or wall stops with architectural drawings.

- END OF SECTION 08 38 00 -

08 38 00 -3